## Slide 1: INTERMEDIATE PROGRAMMING Lesson
By: Droids Robotics
Turn Degrees My Block

## Slide 2: LESSON OBJECTIVES
Create a useful My Block
Learn to make a My Block with Inputs and Outputs
Learn to make a My Block that will take inputs based on measurements with a protractor

## Slide 3: My blocks with inputs and outputs (TURN DEGREES)
See the attached EV3 Files for step-by-step instructions and the actual code for you to learn how to make a useful My Block to turn.
Start at the Stage 1 tab and read all the comments in each one.

## Slide 4: Making a Turn My Block
Just like Move Inches, you can also create a My Block for turns. In Move Inches, we had to figure out how much the robot wheels rotate for one inch on a ruler.
To make a Turn Degrees My Block, you have to figure out how much your rotation sensor on the motor turns for one degree on a protractor
A Turn My Block will be extremely useful to any FLL team because now you can measure your turns using a protractor!!!
45 degree turn by the robot in the real world can be measured with a protractor. We call this protractor degrees.
You can use the EV3 to measure how much your wheel turns. We call this rotation degrees.

## Slide 5: Measuring the Rotation Sensor
The EV3 has a Port View Function which lets it display values measured by sensors
In this section, we will show you how to use the port view to measure turns.
Step 1: Go to Port View on your brick. On the EV3, it is on the third menu to the right. Look for the value for one of your drive motors (motors attached to your wheels)
Step 2: Turn the robot 90 degrees (Pivot Turn) yourself – using your hands to turn one wheel. Make sure the wheels don’t slip when you do this.
Step 3: Look at the rotation degrees value and write down the number of degrees (n)
Step 4: Divide the number from step 3 (n) by 90 (n/90)
This is the number of how many motor rotation degrees are in 1 protractor degree.
You can now use this information to make a Pivot Turn My Block called Turn Degrees. Please see my attached EV3 file. There are Phases marked for you to follow. Once you understand the code, you can modify this code to make a Spin Turn My Block as well.

## Slide 6: STAGE 1: MEASURE TURNS

## Slide 7: STAGE 2: ADD CONSTANTS

## Slide 8: STAGE 3: MAKE My BLOCK

## Slide 9: STAGE 4: USE My BLOCK

## Slide 10: STAGE 5: ANOTHER MY BLOCK

## Slide 11: STAGE 6: TURN DEGREES Right

## Slide 12: STAGE 7: Final Turn DEGREES

## Slide 13: CREDITS
This tutorial was created by Sanjay Seshan and Arvind Seshan from Droids Robotics.
More lessons are available at www.ev3lessons.com
Author’s Email: team@droidsrobotics.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.